## Slide 1: Number Systems
CSE 1108
Introduction to Computer Systems

## Slide 2: Categories of Numbers
Natural Numbers
Whole Numbers
Integers
Rational Numbers
Irrational Numbers

## Slide 3: Natural Numbers
Are the counting numbers
{1, 2, 3, 4, 5, 6, 7, 8, …}

## Slide 4: Whole Numbers
All of the counting numbers and zero.
{0, 1, 2, 3, 4, 5, 6, 7, …}

## Slide 5: Integers
Are all of the natural numbers, their opposites and zero.
{…, -4, -3, -2, -1, 0, 1, 2, 3, 4, …}

## Slide 6: Rational Numbers
Numbers that can be expressed as a fraction (a/b).
This set includes the integers, terminating decimals, and repeating decimals.
Some examples:
2 = 2/1
3 ¼ = 13/4
-0.25 = -25/100
1/3 = 0.33333333333333333333333

## Slide 7: Irrational Numbers
Numbers that CANNOT be expressed as a fraction of integers.
In decimal form, they are the numbers that go on forever without a repeating pattern.
Some examples:
√2 = 1.4142…
π = 3.1415…
45.9492…

## Slide 8: Bridging the Digital Divide
721
234
534
63
935
23
137
275
16
935
145
00100
0101011
10101
010
10010
1101
011011
1101
010
00101101
00100
0101011
011011
1101
00101101
00100
001011
10101
010
10010
1101
011011
1101
010
00101101
00100
0101011
011011
1101
00101
10010
10010
00101101
721
234
534
63
935
23
137
275
16
935
145
Binary-to-Decimal
Conversion
Decimal-to-Binary
Conversion

## Slide 9
But why do we human beings use 10 based number system?

## Slide 10
But why do we human beings use 10 based number system?
The most commonly accepted explanation is that our base-10 number system was adopted by our ancestors most likely because we have 10 fingers.
However, computers operate using the base-2 number system also known as the binary number system.

## Slide 11: The Fundamental Point
Binary representation of numbers and other information is the representation which can be understood by computer chips and can be saved in memory.
In fact, computer chips are made up mostly of semiconductor materials such as silicon.
They can present one of two status at any given time, and can retain a status for a long time.
+5 volt or -5 volt.

## Slide 12: The Fundamental Point
CPU and memory are made up of millions of tiny “switches” that can be either ON or OFF. Two symbols, 0 and 1, can be used to stand for the two states of ON and OFF.

## Slide 13: The Fundamental Point
Since the computer is really made up of tiny switches that can be either OFF or ON, you can look at a binary number as a series of light switches. A 1 represents a switch that is ON, and a 0 means a switch that is OFF.

## Slide 14: Common Number Systems
System | Base | Symbols | Used by humans? | Used in computers?
Decimal | 10 | 0, 1, … 9 | Yes | No
Binary | 2 | 0, 1 | No | Yes
Octal | 8 | 0, 1, … 7 | No | No
Hexa- decimal | 16 | 0, 1, … 9, A, B, … F | No | No

## Slide 15: Quantities/Counting (1 of 2)
Decimal | Binary | Octal | Hexa- decimal
0 | 0 | 0 | 0
1 | 1 | 1 | 1
2 | 10 | 2 | 2
3 | 11 | 3 | 3
4 | 100 | 4 | 4
5 | 101 | 5 | 5
6 | 110 | 6 | 6
7 | 111 | 7 | 7

## Slide 16: Quantities/Counting (2 of 2)
Decimal | Binary | Octal | Hexa- decimal
8 | 1000 | 10 | 8
9 | 1001 | 11 | 9
10 | 1010 | 12 | A
11 | 1011 | 13 | B
12 | 1100 | 14 | C
13 | 1101 | 15 | D
14 | 1110 | 16 | E
15 | 1111 | 17 | F

## Slide 17: Conversion Among Bases
The possibilities:
Hexadecimal
Decimal
Octal
Binary

## Slide 18: Quick Example
2510 = 110012 = 318 = 1916
Base

## Slide 19: Decimal to Decimal (just for fun)
Hexadecimal
Decimal
Octal
Binary

## Slide 20
12510 => 5 x 100 = 5 2 x 101 = 20 1 x 102 = 100 125
Base
Weight

## Slide 21: Binary to Decimal
Hexadecimal
Decimal
Octal
Binary

## Slide 22: Binary to Decimal
Technique
  Multiply each bit by 2n, where n is the “weight” of the bit
  The weight is the position of the bit, starting from 0 on the right
  Add the results

## Slide 23: Example
1010112 => 1 x 20 = 1 1 x 21 = 2 0 x 22 = 0 1 x 23 = 8 0 x 24 = 0 1 x 25 = 32
4310
Bit “0”

## Slide 24: Octal to Decimal
Hexadecimal
Decimal
Octal
Binary

## Slide 25: Octal to Decimal
Technique
  Multiply each bit by 8n, where n is the “weight” of the bit
  The weight is the position of the bit, starting from 0 on the right
  Add the results

## Slide 26: Example
7248 => 4 x 80 = 4 2 x 81 = 16 7 x 82 = 448 46810

## Slide 27: Hexadecimal to Decimal
Hexadecimal
Decimal
Octal
Binary

## Slide 28: Hexadecimal to Decimal
Technique
  Multiply each bit by 16n, where n is the “weight” of the bit
  The weight is the position of the bit, starting from 0 on the right
  Add the results

## Slide 29: Example
ABC16 => C x 160 = 12 x 1 = 12 B x 161 = 11 x 16 = 176 A x 162 = 10 x 256 = 2560
274810

## Slide 30: Decimal to Binary
Hexadecimal
Decimal
Octal
Binary

## Slide 31: Decimal to Binary
Technique
  Divide by two, keep track of the remainder
  First remainder is bit 0 (LSB, least-significant bit)
  Second remainder is bit 1
  Etc.

## Slide 32: Example
12510 = ?2
2 125 62 1
2 31 0
2 15 1
2 7 1
2 3 1
2 1 1
2 0 1
12510 = 11111012

## Slide 33: Octal to Binary
Hexadecimal
Decimal
Octal
Binary

## Slide 34: Octal to Binary
Technique
  Convert each octal digit to a 3-bit equivalent binary representation

## Slide 35: Example
7058 = ?2
7 0 5
111 000 101
7058 = 1110001012

## Slide 36: Hexadecimal to Binary
Hexadecimal
Decimal
Octal
Binary

## Slide 37: Hexadecimal to Binary
Technique
  Convert each hexadecimal digit to a 4-bit equivalent binary representation

## Slide 38: Example
10AF16 = ?2
1 0 A F
0001 0000 1010 1111
10AF16 = 00010000101011112

## Slide 39: Decimal to Octal
Hexadecimal
Decimal
Octal
Binary

## Slide 40: Decimal to Octal
Technique
  Divide by 8
  Keep track of the remainder

## Slide 41: Example
123410 = ?8
8 1234
154 2
8
19 2
8
2 3
8
0 2
123410 = 23228

## Slide 42: Decimal to Hexadecimal
Hexadecimal
Decimal
Octal
Binary

## Slide 43: Decimal to Hexadecimal
Technique
  Divide by 16
  Keep track of the remainder

## Slide 44: Example
123410 = ?16
123410 = 4D216
16 1234
77 2
16
4 13 = D
16
0 4

## Slide 45: Binary to Octal
Hexadecimal
Decimal
Octal
Binary

## Slide 46: Binary to Octal
Technique
  Group bits in threes, starting on right
  Convert to octal digits

## Slide 47: Example
10110101112 = ?8
1 011 010 111
1 3 2 7
10110101112 = 13278

## Slide 48: Binary to Hexadecimal
Hexadecimal
Decimal
Octal
Binary

## Slide 49: Binary to Hexadecimal
Technique
  Group bits in fours, starting on right
  Convert to hexadecimal digits

## Slide 50: Example
10101110112 = ?16
10 1011 1011
B B
10101110112 = 2BB16

## Slide 51: Octal to Hexadecimal
Hexadecimal
Decimal
Octal
Binary

## Slide 52: Octal to Hexadecimal
Technique
  Use binary as an intermediary

## Slide 53: Example
10768 = ?16
1 0 7 6
001 000 111 110
2 3 E
10768 = 23E16

## Slide 54: Hexadecimal to Octal
Hexadecimal
Decimal
Octal
Binary

## Slide 55: Hexadecimal to Octal
Technique
  Use binary as an intermediary

## Slide 56: Example
1F0C16 = ?8
1 F 0 C
0001 1111 0000 1100
1 7 4 1 4
1F0C16 = 174148

## Slide 57: Exercise – Convert ...
Don’t use a calculator!
Decimal | Binary | Octal | Hexa- decimal
33 |  |  | 
 | 1110101 |  | 
 |  | 703 | 
 |  |  | 1AF

## Slide 58: Exercise – Convert …
Decimal | Binary | Octal | Hexa- decimal
33 | 100001 | 41 | 21
117 | 1110101 | 165 | 75
451 | 111000011 | 703 | 1C3
431 | 110101111 | 657 | 1AF
Answer

## Slide 59: Fractions
Decimal to decimal (just for fun)
3.14 => 4 x 10-2 = 0.04 1 x 10-1 = 0.1 3 x 100 = 3 3.14

## Slide 60: Fractions
Binary to decimal
10.1011 => 1 x 2-4 = 0.0625 1 x 2-3 = 0.125 0 x 2-2 = 0.0 1 x 2-1 = 0.5 0 x 20 = 0.0 1 x 21 = 2.0 2.6875

## Slide 61: Fractions
Decimal to binary
3.14579
.14579 x 2 0.29158 x 2 0.58316 x 2 1.16632 x 2 0.33264 x 2 0.66528 x 2 1.33056
etc.
11.001001...

## Slide 62: Exercise – Convert ...
Don’t use a calculator!
Decimal | Binary | Octal | Hexa- decimal
29.8 |  |  | 
 | 101.1101 |  | 
 |  | 3.07 | 
 |  |  | C.82

## Slide 63: Exercise – Convert …
Decimal | Binary | Octal | Hexa- decimal
29.8 | 11101.110011… | 35.63… | 1D.CC…
5.8125 | 101.1101 | 5.64 | 5.D
3.109375 | 11.000111 | 3.07 | 3.1C
12.5078125 | 1100.10000010 | 14.404 | C.82
Answer

## Slide 64: Thank you! Any Questions?