## Slide 1: Microcontroller Based System Design
CSE 3216
LAB 1

## Slide 2: Course Teachers:
Ashna Nawar Ahmed
Lecturer
Department of CSE
AUST
Email: ashna.cse@aust.edu
Phone: 01710812206
Farzad Ahmed
Lecturer
Department of CSE
AUST
Email: farzad.cse@aust.edu
Phone: 01685245342

## Slide 3: Google Classroom Code
v3t5p5x

## Slide 4: Hardware Project Criteria
Must be beneficial to society
Should be budget friendly
Must be a team project
Each team member must contribute to the project

## Slide 5
Lab 1
Introduction to MSD Lab
Lecture
Lab 2
Lecture
Lab 3
Lecture
Lab 4
Lab 5
Lab 6
Lab 7
Group formation
Project Proposal Submission
Lecture
Lecture
Project Submission
Presentation + Report + Final Project + Viva
Presentation + Report

## Slide 6: What is Arduino?
Arduino is an open-source electronics platform based on easy-to-use hardware and software.
Arduino boards are able to read inputs - light on a sensor, and turn it into an output - activating a motor.
You can tell your board what to do by sending a set of instructions to the microcontroller on the board. To do so you use the Arduino programming language and the Arduino Software (IDE).

## Slide 7: Different Types of Arduino Boards
Arduino UNO-> 14 digital pins, 6 analog pins
Arduino MEGA-> 54 digital pins, 16 analog pins

## Slide 8
Arduino UNO Pin Diagram

## Slide 9
Arduino MEGA Pin Diagram

## Slide 10: Arduino programming language
Arduino programming language can be divided in three main parts:
        structure,
        values (variables and constants), and
        functions.

## Slide 11: Structure of Arduino Code

## Slide 12: The elements/structure of Arduino (C++) code:

## Slide 13: Functions of Arduino Code

## Slide 14: FUNCTIONS of arduino
  For controlling the Arduino board and performing computations.
  Digital I/O
digitalRead() digitalWrite() pinMode()

## Slide 15: digitalRead()
Description
Reads the value from a specified digital pin, either HIGH or LOW.
Syntax
digitalRead(pin)
Parameters
pin: the number of the digital pin you want to read
Returns
HIGH or LOW

## Slide 16: digitalWrite()
Description
Write a HIGH or a LOW value to a digital pin.
Syntax
digitalWrite(pin, value)
Parameters
pin: the pin number
value: HIGH or LOW
Returns
Nothing

## Slide 17: pinMode()
Description
Configures the specified pin to behave either as an input or an output.
Syntax
pinMode(pin, mode)
Parameters
pin: the number of the pin whose mode you wish to set
mode: INPUT, OUTPUT

## Slide 18: Basic Arduino Code
The bare minimum of code needed to start an Arduino sketch.
void setup() {
// put your setup code here, to run once:
}
void loop() {
// put your main code here, to run repeatedly:
}

## Slide 19: Blinking LED
int ledpin = 12;
void setup() {
pinMode(ledpin,OUTPUT);
}
void loop() {
digitalWrite(ledpin,HIGH);
delay(500);
digitalWrite(ledpin,LOW);
delay(500);
}

## Slide 20: How to connect LED to Arduino UNO

## Slide 21: Task for Students
Connect 3 LEDs to Arduino, and make them blink in different patterns on a loop.
LED1 -> LED2 -> LED3 -> LED2 -> LED1
LED1 -> LED2 -> LED2 -> LED3 -> LED3 -> LED3

## Slide 22: THE END