## Slide 1: MICROCONTROLLER BASED SYSTEM DESIGN
CSE 3216
Lab 6
AUST CSE

## Slide 2: Today’s Contents:
LCD
IR SENSOR
PIR SENSOR

## Slide 3: LCD (Liquid Crystal Display)

## Slide 4: LCD
LCD Model we will use in proteus
LCD Model with Pin Description

## Slide 5
Pin No.-> Pin Name | Pin Description | Pin Connection
1-> VSS | Ground Pin | Connect to ground
2-> VDD | VCC pin(for power) | Connect to power supply i.e. 5V
3-> VEE | Adjusts contrast of LCD | Could be connected to a variable POT that can vary the voltage between 0 to 5V, but here we will simply connect it to 5V
4-> RS | Register Select: Toggles between Command/Data Register | Connected to an Arduino pin and gets either 0 or 1. 0 -> Command Mode 1-> Data Mode
5-> RW | Read/Write: Toggles the LCD between Read/Write Operation | If connected to an Arduino pin, it will get either 0 or 1. 0 -> Write Operation 1-> Read Operation However, as Read operation is rarely needed, we typically directly connect it to GND so it will always get 0.
6-> E | Enable: Must be held high to perform Read/Write Operation | Connected to an Arduino pin and always gets 1(HIGH).
(7-14)-> (D0-D7) | Data Bits (0-7): Pins used to send Command or data to the LCD. | In 4-Wire Mode Only 4 pins (0-3) is connected to Arduino In 8-Wire Mode All 8 pins(0-7) are connected to Arduino
15-> LED + [Not present in the model we are using] | LED Positive: used to turn on/off backlight of the LCD | Connect to power supply i.e. 5V [not needed here]
16-> LED - [Not present in the model we are using] | LED Negative: used to turn on/off backlight of the LCD | Connect to ground [not needed here]

## Slide 6: LCD (contd.)
4-bit and 8-bit Mode of LCD:
The LCD can work in two different modes, namely the 4-bit mode and the 8-bit mode. In 4 bit mode we send the data nibble by nibble, first upper nibble and then lower nibble. A nibble is a group of four bits, so the lower four bits (D0-D3) of a byte form the lower nibble while the upper four bits (D4-D7) of a byte form the higher nibble. This enables us to send 8 bit data.
Whereas in 8 bit mode we send data byte by byte, so we can send the 8-bit data directly in one stroke since we use all the 8 data lines.
8-bit mode is faster and flawless than 4-bit mode. But the major drawback is that it needs 8 data lines connected to the microcontroller. This will make us run out of I/O pins on our Arduino board, so 4-bit mode is widely used. No control pins are used to set these modes. It's just the way of programming that change.

## Slide 7: Add Libraries
Add the libraries for IR, PIR and Ultrasonic sensors to the library folder of Proteus Software:
In C:\ProgramData\Labcenter Electronics\Proteus 8 Professional\LIBRARY
OR
In C:\Program Files (x86)\Labcenter Electronics\Proteus 8 Professional\LIBRARY

## Slide 8: Infrared Sensor (Active)

## Slide 9: IR SENSOR

## Slide 10: IR SENSOR
3 pins: positive voltage(+Vcc), ground(GND) and output voltage(Vout)
Emits light in order to sense surrounding objects
Consists of: emitter(IR source) and detector(IR detector)
Emitter: IR LED-> Emits IR light
Detector: IR photodiode-> Sensitive to IR light of the same wavelength which is emitted by the IR LED
Output determined based on intensity of reflection received by photodiode
Output is binary

## Slide 11: IR SENSOR
IR Transmitter or IR LED
IR Receiver or Photodiode

## Slide 12: Infrared Sensor (Passive)

## Slide 13: PIR SENSOR

## Slide 14: PIR SENSOR
3 pins: positive voltage(+Vcc), ground(GND) and output voltage(Vout)
Can detect thermal radiation of objects in the infrared range
Consists of: 1 pair of pyroelectric sensors, to detect heat energy in the surrounding environment
Sensors housed within a series of lenses
Purpose of lens: widening the device’s sensing area
Output is binary

## Slide 15: IR vs. PIR: COMPARISON
IR SENSOR
Contains active emitter
Capable of detecting exact position of objects
Used in: garage door systems, industrial settings
PIR SENSOR
No active emitter
Capable of detecting motion
Used in: security alarms and automatic lighting setups

## Slide 16: THE END