## Slide 1: MICROCONTROLLER BASED SYSTEM DESIGN
CSE 3215
Lecture 3

## Slide 2: Popular Microcontroller Technologies or families
8051 Microcontroller:
The most universally employed set of microcontrollers come from the 8051 family. The original 8051 microcontroller was initially invented by Intel. The two other members of this 8051 family are-

8052 – This microcontroller has 3 timers & 256 bytes of RAM. Additionally, it has all the
features of
the traditional 8051 microcontroller. 8051 microcontroller is a subset of 8052

microcontroller.
8031 – This microcontroller is ROM less, other than that it has all the features of a traditional 8051 microcontroller. For execution an external ROM of size 64K bytes can be added to its chip.

## Slide 3: Popular Microcontroller Technologies or families
8051 Microcontroller:
Even though Intel developed 8051 Microcontrollers, more than 20 semiconductor manufacturers are
still producing 8051 compatible microcontrollers i.e. processors based on MSC-51 Architecture.
Some of the 8051 Microcontrollers produced by different manufacturers are: Atmel (AT89C51, AT89S51), Phillips (S87C654), STC Micro (STC89C52), Infineon (SAB-C515, XC800), Siemens (SAB- C501), Silicon Labs (C8051), NXP (NXP700, NXP900), etc.

## Slide 4: 8051 Family

## Slide 5: Popular Microcontroller Technologies or families
8051 Microcontroller Architecture:
8051 is an 8 – bit Microcontroller i.e. the data bus of the 8051 Microcontroller (both internal and external) is 8 – bit wide. It is a CISC based Microcontroller with Harvard Architecture (separate program and data memory).
CPU, ROM, RAM, etc. the 8051
Since the basic layout of a microcontroller includes a
microcontroller also has a similar layout.
Special Function Registers (SFRs) of 128 bytes.
32 I/O pins arranged as four 8-bit ports (P0 - P3)
Two 16-bit timer/counters : T0 and T1
Two external and three internal vectored interrupts
One full duplex serial I/O

## Slide 6: Popular Microcontroller Technologies or families
PIC Microcontroller
PIC is a family of microcontrollers made by Microchip Technology, derived from the PIC1650 originally developed by General Instrument. The name PIC initially referred to ”Peripheral Interface Controller”, then it was corrected as ”Programmable Intelligent Computer”.
Early models of PIC had read-only memory (ROM) or field-programmable EPROM for program storage, some with provision for erasing memory. All current models use flash memory for program storage, and newer models allow the PIC to reprogram itself.
Program memory and data memory are separated. Data memory is 8-bit, 16-bit, and, in latest models, 32-bit wide.
Program instructions vary in bit-count by family of PIC, and may be 12, 14, 16, or 24 bits long. The instruction set also varies by model.

## Slide 7: Popular Microcontroller Technologies or families
PIC Microcontroller Architecture:
PIC Microcontroller architecture is based on Harvard architecture and supports RISC architecture (Reduced Instruction Set Computer).
PIC microcontroller architecture consists of memory organization (RAM, ROM, stack), CPU, timers, counter, ADC, DAC, serial communication, CCP (Capture/Compare/PWM) module and I/O ports.
PIC microcontroller also supports the protocols like CAN (Controller Area Network), SPI(Serial
Receiver/Transmitter) for
Peripheral Interface), UART (Universal Synchronous/Asynchronous interfacing with other peripherals.


## Slide 8: Popular Microcontroller Technologies or families
Microchip offers five main families of microcontrollers, whose features are summarized in Table. Every member of any one family shares the same core architecture and instruction set.
PIC family | Stack size (words) | Instruction word size | Number of instructions | Interrupt vectors
12CXXX/12FXXX | 2 | 12 or 14-bit | 33 | None
16C5XX/16F5XX | 2 | 12-bit | 33 | None
16CXXX/16FXXX | 8 | 14-bit | 35 | 1
17CXXX | 16 | 16-bit | 58 | 4
18CXXX/18FXXX | 32 | 16-bit | 75 | 2

## Slide 9: Popular Microcontroller Technologies or families
Microchip also used to give each family a name.
Thus, their first family, the 16C5XX, was called the ‘baseline’ family.
The development of this, with device numbers starting ‘16C’ or ‘16F’ (and a fourth digit that was
not 5), was called the ‘mid-range’ family.
The powerful evolution of this, with codes starting ‘17C’,was called the ‘high-end’ family.

## Slide 10: Popular Microcontroller Technologies or families
ARM Microcontroller
ARM, Advanced RISC Machine, is a family of reduced instruction set
computing (RISC) architectures for computer processors, configured for various environments.
It was first introduced by the Acron computers’ organization.
ARM processors are extensively used in consumer electronic devices such as smartphones, tablets, multimedia players and other mobile devices. Because of their reduced instruction set, they require fewer transistors, which enables a smaller die size for the integrated circuitry (IC).
The ARM processor’s smaller size, reduced complexity and lower power consumption makes them suitable for increasingly miniaturized devices.

## Slide 11: Popular Microcontroller Technologies or families
ARM Microcontroller Architecture:
The ARM architecture is a 32-bit RISC processor developed by ARM Ltd. Owing to its power-
in the mobile electronics
saving attributes, ARM central processing units are prevailing marketplace, where less power expenditure is a vital design aim.
ARM processor features include:
Load or store architecture.
An orthogonal instruction set.
Mostly single-cycle execution.
Enhanced power-saving design.
Preset instruction width of 32 bits so as to simplify pipe-lining and decoding, at minimized code density.

## Slide 12: Orthogonal instruction set
architecture where all instruction types can use all addressing modes. It
In computer engineering, an orthogonal instruction set is an instruction set
is
"orthogonal" in the sense that the instruction type and the addressing mode vary independently.

## Slide 13: Popular Microcontroller Technologies or families
AVR Microcotroller
The basic architecture of AVR was designed by two students of Norwegian Institute of Technology (NTH), Alf Egil Bogen and Vegard Wollan, and then was bought and developed by Atmel in 1996.
Atmel says that it is nothing more than a product name, but it might stand for Advanced Virtual RISC or Alf and Vegard RISC.
The AVR was one of the first microcontrollers to use on chip Flash memory for program storage.
Flash memory is a non-volatile programmable memory, ideal for fast development because Flash memory can be erased in seconds compared to the 20 minutes or more needed for the UV-EPROM.

## Slide 14: Popular Microcontroller Technologies or families
AVR Microcontroller
There are many kinds of AVR microcontroller with different properties. Except for AVR32, which is a 32 bit microcontroller, AVRs are all 8-bit microcontrollers, meaning that the CPU can work on only 8 bits of data at a time. Data larger then 8 bits has to be broken into 8-bit pieces to be processed by the CPU.
AVRs are generally classified into four broad groups:
  Mega
  Tiny
  Special purpose
  Classic

## Slide 15: Features of a Microcontroller
CPU:
Microcontrollers brain is named as CPU. CPU is the device which is employed to fetch data, decode it and at the end complete the assigned task successfully. With the help of CPU all the components of microcontroller are connected into a single system. Instruction fetched by the programmable memory is decoded by the CPU.
Memory:
In a microcontroller memory chip works same as microprocessor. Memory chip stores all programs & data. Microcontrollers are built with certain amount of ROM or RAM (EPROM, EEPROM etc) or flash memory for the storage of program source codes.

## Slide 16: Features of a Microcontroller
Memory Types
EPROM ( Erasable Programmable Read-Only Memory):
It is a type of memory chip that retains its data when its power supply is switched off. Once programmed, an EPROM can be erased by exposing it to strong ultraviolet light source.
EEPROM (Electrically Erasable Programmable Read Only Memory):
Many microcontrollers have limited amounts of EEPROM on the chip. EEPROM seems more suited (because of its economics) for small amounts of memory that hold a limited number of parameters that may have to be changed from time to time. This type of memory is relatively slow, and the number of erase/write cycles allowed in its lifetime is limited.

## Slide 17: Features of a Microcontroller
FLASH (EPROM)
Flash provides a better solution than regular EEPROM when there is a requirement for large amounts of non-volatile program memory. It is both faster and permits more erase/write cycles than EEPROM.
MASK ROM
Mask ROM refers to a kind of ROM in which the contents are programed by the IC manufacturer. In other words, it is not a user-programmable ROM. The term mask is used in IC fabrication. Since the process is costly, mask ROM is used when the needed volume is high and it is absolutely certain that the contents will not change.
It is common practice to use UV-EPROM or Flash for the development phase of a project, and only after the code/data have been finalize is the mask version of the product is ordered.

## Slide 18: Features of a Microcontroller
Input/Output ports:
Input/output(I/O) ports are necessary for interfacing various I/O devices. Microcontrollers are provided with a limited number of I/O ports for interfacing necessary I/O devices without any additional hardware.
Moreover, multifunctional capability is provided so that many driver functions such as interfacing external memory, interrupt inputs etc can be provided with a limited number of I/O pins.

## Slide 19: Features of a Microcontroller
Timers:
A microcontroller may be in-built with one or more timer or counters. The timers & counters control all counting & timing operations within a microcontroller. Timers are employed to count external pulses.
The main operations performed by timers are-
pulse generations
clock functions
frequency measuring
modulations
making oscillations

## Slide 20: Features of a Microcontroller
ADC :
Stands for "Analog-to-Digital Converter." Since computers only process digital information, they require digital input. Therefore, if an analog input is sent to a computer, an analog-to-digital converter (ADC) is required. This device can take an analog signal, such as an electrical current, and digitize it into a binary format that the computer can understand.
DAC:
Stands for "Digital-to-Analog Converter“. This converter executes opposite functions that ADC perform. This device is generally employed to supervise analog appliances like- DC motors, etc.

## Slide 21: Features of a Microcontroller
Watchdog Timer (WDT) Reset:
A watchdog timer (WDT) is a hardware timer that automatically generates a system reset if the main program neglects to periodically service it. It is often used to automatically reset an embedded device that hangs because of a software or hardware fault.

## Slide 22: Features of a Microcontroller
Working Procedure of Watchdog Timer—
After the initialization, the microcontroller remains in an infinite loop. Within the loop, a few instructions are embedded as part of the main program, which resets a timer, known a “Watchdog Timer”, which is initialized with a time-out parameter longer than the worst-case time to go around the loop.
The timer acts as a resetable timer– each time the program goes around the loop, the timer is reset before it reaches time-out.
However, when the system goes astray, that is the microcontroller is no longer executing the loop, the watchdog timer is not reseted and it proceeds towards time-out.
When the watchdog timer reaches the end of time out interval, the timer output resets the microcontroller bringing it back to the predefined initial state.
So, a watchdog timer plays a very important role in the case of embedded systems where there is no human access.

## Slide 23: Features of a Microcontroller
Fast Context Switching:
Microcontrollers are used in many real-time applications. A real-time application is one that requires ‘timely’ response from the microcontroller.
These real-time systems are event-driven with the help of interrupts. For faster response, the time required for switching from one task to another should be small. It is known that the contents of various registers used by a task are stored in the stack before switching to another task and when the processor reverts to the previous task, the contents of the registers are restored from the stack.
These storing and restoring operations usually take long time, which may not be acceptable for many real time applications.

## Slide 24: Features of a Microcontroller
Register banks can be used to achieved fast context switching. One of the register banks is accessible at any point of time.
A particular register bank, consisting of a set of registers, is used by a particular task. When the processor switches from one task to the other, the flag bits of the special function register are simply changed to assign a new register bank. This avoids the time-consuming storing and restoring of register contents in stack during context switching.

## Slide 25: Features of a Microcontroller
Powerful Interrupt Structure:
Interrupt is a mechanism by which a processor comes out of the program sequence it is executing at a particular instant and jumps to a specific location corresponding to a particular source of interrupt.
Microcontrollers are provided with a powerful interrupt structure with a provision for programmable priority levels and enabling/disabling capability of all the interrupts in individual levels.

## Slide 26: THANK YOU