## Slide 1: Digital System Design
Lecture - 5

## Slide 2: Booth’s Multiplication Algorithm
Booth’s multiplication algorithm can be implemented by repeatedly adding one of two predetermined values A and S to a product P, then performing a rightward arithmetic shift on P.
Let m and r be the multiplicand and multiplier respectively. And let x and y represent the number of bits in m and r.
  Now do the next consecutive steps.

## Slide 3: Booth’s Multiplication Algorithm (Contd.)
Determine the values of A and S, and the initial value of P. All of these numbers should have a length equal to (x + y + 1).
  A: Fill the most significant (left most) bits with the value of m. Fill the remaining (y + 1) bits with zeros.
  S: Fill the most significant bits with the value of (-m) in 2’s complement notation. Fill the remaining (y + 1) bits with zeros.
  P: Fill the most significant x bits with zeros. To the right of this, append the value of r. Fill the least significant (right most) bit with a zero.

## Slide 4: Booth’s Multiplication Algorithm (Contd.)
2. Determine the two least significant bits of P.
  If they are 01, find the value of P + A. Ignore any overflow.
  If they are 10, find the value of P + S. Ignore any overflow.
  If they are 00, do nothing, use P directly in the next step.
  If they are 11, do nothing, use P directly in the next step.

## Slide 5: Booth’s Multiplication Algorithm (Contd.)
3. Arithmetically shift the value obtained in the second step by a single place to the right. Now, let P equals this new value.
4. Repeat steps 2 and 3 until they have been done y times.
5. Drop the least significant (right most) bit from P.
This is the final product of m and r.